## Slide 1: Deeper Assembly: Addressing, Conditions, Branching, and Loops
Some material taken from Assembly Language for x86 Processors by Kip Irvine © Pearson Education, 2010
Slides revised 2/13/2014 by Patrick Kelley

## Slide 2: Overview
Data Transfer Instructions
Addition and Subtraction
Indirect Addressing
JMP and BRANCH Instructions

## Slide 3
Data Transfer Instructions
Operand Types
Direct Memory Operands
move/load/store Instructions
Zero & Sign Extension

## Slide 4
Operand Types
Imm (immediate) – a constant value
Label – address specified by a label
R(t,s,d) – Contents of a register
(R) – Contents of memory pointed to by a register.
offset(R) – Contents pointed to by R + offset
Examples:
li $v0, 0x4f # Imm into register $v0
la $a0, mynum # label into register $a0
lw $ra, 12($sp) # data at $sp + 12 into $ra

## Slide 5
Direct Memory Operands
MIPS, unlike some architectures, does not support direct memory addressing
Instead you must set up your memory accesses.
  Point to the data by loading the address into a register: la $a0, myVar
  Now you can access myVar with an offset to the address: lw $a1, 0($a0) # load myVar into a1
Note that it was Ok that the offset was 0, but we could also use a non-zero offset if we needed, for instance to access elements of an array.

## Slide 6
Move, Load, and Store
Load and Store are the memory access operations
  There are several variations of each based on data size and type. (lb, lbu, lwl, sh, sw, etc.)
  There are also load variations that don’t affect data directly (la, li)
Move is used to transport data between registers only and never affects memory
Variations on Move are use to access special registers.

## Slide 7
Zero- and Sign- extension
Extension is used when a small piece of data is stored into a larger space. (ex. byte into word.)
The space to the left is filled with either zero or the sign bit.
Address operations sign extend the offset before ORing it to the base.
Arithmetic operations select which to use by type:
  Unsigned operations zero-extend
  Signed operations sign-extend

## Slide 8
What's Next
Data Transfer Instructions
Addition and Subtraction
Indirect Addressing
JMP and BRANCH Instructions

## Slide 9
ADD and SUB Instructions
add or addu Rd, Rs, Rt
  Logic: destination  source Rs + source Rt
sub or subu Rd, Rs, Rt
  Logic: destination  source Rs – source Rt
addi or addiu Rd, Rs, Imm
  Logic: destination  source Rs + immediate
Note that memory is not affected by these operations

## Slide 10
Negate
neg or negu Rd, Rs
  Logic: destination  0 - source Rs
  negu does not give exception if you try to negate maximum negative
Subtract operations are really a convenience, not needed since you can negate and add a number to get the same effect.
However, negate in MIPS is implemented by doing a subtraction, so it actually would add a step.

## Slide 11
What's Next
Data Transfer Instructions
Addition and Subtraction
Indirect Addressing
JMP and BRANCH Instructions

## Slide 12
Indirect Addressing
Recall that some operations take an offset and base as an operand
We can store the base address of a data structure, like an array, in a register.
Then we can refer to individual elements by adding an offset to the base address.
  This works well when offsets are known and the elements are few, as in stack frames.
  But since the offset must be a constant, it is cumbersome to use for long lists.
An example is on the following slide:

## Slide 13
# TITLE Add and Subtract (AddSub2.s)
# This program adds and subtracts 32-bit integers.
# It uses offsets to get to the variables
.data
# variables
Nums: .word 0x1000
.word 0x5000
.word 0x3000
Sum: .word 0
.text
.globl main
main: # start of the main procedure
la $a0, Nums # Put the base address in $a0
lw $t0, 0($a0) # Put first number into $t0
lw $t1, 4($a0) # Put second number into $t1
lw $t2, 8($a0) # Put third number into $t2
add $t4, $t0, $t1 # Add first two numbers, put in $t4
sub $t4, $t4, $t2 # Subtract third number from result
sw $t4, Sum # Put result in sum
jr $ra # return to caller (exit program)
Example: Using indirect addressing

## Slide 14
Indirect Addressing (cont.)
A better way is to iterate through a list by adding to the base address.
If the list contains complex data, we can create a list of base addresses (pointers) and iterate through those.
Using base addresses as simple pointers (without an offset) also works well for structures like linked lists and queues.

## Slide 15
What's Next
Data Transfer Instructions
Addition and Subtraction
Indirect Addressing
JMP and BRANCH Instructions

## Slide 16
Program Flow
A processor does operations sequentially
  The Fetch – Decode – Execute cycle gets instructions in order
  If we wish to change the program flow, we need a special instruction
Jump instructions are unconditional
  Equivalent to a ‘goto’ statement.
  Used to call subroutines or functions
  May jump to a label or address in register
Branch instructions are tied to a condition
  Similar in effect to an ‘if – then – else’ construct
  Always branch to a label

## Slide 17
Jump Instruction
top:
.
.
j top
J is an unconditional jump to a label that is usually within the same procedure.
Syntax: j Label
Logic: IR  Label
Example:

## Slide 18
Conditional Branching
In some processors, each instruction sets status flags in the processor
  Usually in a status register with a bit for each flag
  Typical flags are sign, carry, overflow, zero, and parity
There is a certain efficiency in that we don’t have to test a result if the flags are already set
Ex: mov AX, 5 sub AX, 5 jz goHereIfZero
… # else continue on

## Slide 19
Conditional Branching (cont.)
MIPS tests conditions as part of the Branch instruction
No need for the overhead of maintaining status flags
Also fewer instructions to needed in the architecture
But branch instructions take a little longer because they have to do the test first
Ex: li $S1, -5 add $S1, $S1, 5 beq $zero, $S1, goHereIfZero
… # else continue on

## Slide 20
Applications (1 of 5)
bgtu $V0, $V1, Larger
Task: Jump to a label if unsigned $V0 is greater than $V1
Solution: Use bgtu
bgt $V0, $V1, Larger
Task: Jump to a label if signed $V0 is greater than $V1
Solution: Use bgt

## Slide 21
Applications (2 of 5)
lw $V1, Val1
bleu $V0, $V1, L1 # below or equal
Jump to label L1 if unsigned $V0 is less than or equal to Val1
lw $V1, Val1
ble $V0, $V1, L1 # below or equal
Jump to label L1 if signed $V0 is less than or equal to Val1

## Slide 22
Applications (3 of 5)
  sw $V1, Large
  bleu $V0, $V1, Next
  sw $V0, Large
Next:
Compare unsigned $V0 to $V1, and copy the larger of the two into a variable named Large
  sw $V0, Small
  bge $V0, $V1, Next
  sw $V1, Small
Next:
Compare signed $V0 to $V1, and copy the smaller of the two into a variable named Small

## Slide 23
Applications (4 of 5)
  lw $V0, ($a0)
  beq $V0, $0, L1
  **OR**
  beqz $V0, L1
Jump to label L1 if the memory word pointed to by $A0 equals Zero
  lw $V0, ($a0)
andi $V0, $V0, 1
beqz $V0, L2
Jump to label L2 if the word in memory pointed to by $A0 is even

## Slide 24
Applications (5 of 5)
li $S1, 0x0000000B
and $S0, $S0, $S1 ; clear unwanted bits
beq $S0, $S1, L1 ; check remaining bits
Task: Jump to label L1 if bits 0, 1, and 3 in $S0 are all set.
Solution: Clear all bits except bits 0, 1,and 3. Then compare the result with 0000000B in hex.

## Slide 25
Encrypting a String (do until)
# The encryption key is 232, can be any byte value
# We’ll use an arbitrary string size of 128
.data
Buffer: .space 129
bufSize: .word 128
.text
  lw $a0, bufSize # loop counter
  la $a1, Buffer # point to buffer
L1:
lbu $a3, ($a1) # get a byte
  xori $a3, $a3, 232 # translate a byte
  sb $a3, ($a1) # store translated byte
  addi $a0, $a0, -1 # decrement loop counter
  beqz $a0, Next # if done, leave loop
  addi $a1, $a1, 1 # point to next byte
  j L1 # loop
Next:
The following loop uses the XOR instruction to transform every character in a string into a new value.

## Slide 26
Encrypting a String (while, for)
# The encryption key is 232, can be any byte value
# We’ll use an arbitrary string size of 128
.data
Buffer: .space 129
bufSize: .word 128
.text
  lw $a0, bufSize # loop counter
  la $a1, Buffer # point to buffer
L1:
    blez $a0, Next # if done, leave loop
lbu $a3, ($a1) # get a byte
  xori $a3, $a3, 232 # translate a byte
  sb $a3, ($a1) # store translated byte
  addi $a0, $a0, -1 # decrement loop counter
  addi $a1, $a1, 1 # point to next byte
  j L1 # loop
Next:
The following loop uses the XOR instruction to transform every character in a string into a new value.

## Slide 27
Block-Structured IF Statements
Assembly language programmers can easily translate logical statements written in C++/Java into assembly language. For example:
  lw $a0, op1
  lw $a1, op2
  bne $a0, $a1, L1
  li $a3, 1
  sw $a3, X
  j L2
  L1: li $a3, 2
  sw $a3, X
L2:
if( op1 == op2 )
X = 1;
else
X = 2;

## Slide 28
Compound Expression with AND (1 of 3)
When implementing the logical AND operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is false, the second expression is skipped:
if (al > bl) AND (bl > cl)
X = 1;

## Slide 29
Compound Expression with AND (2 of 3)
# al, bl, and cl are in $a0, $a1, and $a2
# repsectively; $a3 holds 1
bgt $a0, $a1, L1 # first expression...
j next
L1:
bgt $a1, $a2, L2 # second expression...
j next
L2: # both are true
sw $a3, X # set X to 1
next:
if (al > bl) AND (bl > cl)
X = 1;
This is one possible implementation . . .
*Note that the branches could have been bgtu.

## Slide 30
Compound Expression with AND (3 of 3)
# al, bl, and cl are in $a0, $a1, and $a2
# repsectively; $a3 holds 1
ble $a0, $a1, next # first expression...
# quit if false
ble $a1, $a2, next # second expression...
# quit if false
sw $a3, X # both are true
next:
if (al > bl) AND (bl > cl)
X = 1;
But the following implementation uses 40% less code by reversing the first relational operator. We allow the program to "fall through" to the second expression:

## Slide 31
Compound Expression with OR (1 of 2)
When implementing the logical OR operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is true, the second expression is skipped:
if (al > bl) OR (bl > cl)
X = 1;

## Slide 32
Compound Expression with OR (2 of 2)
# al, bl, and cl are in $a0, $a1, and $a2
# repsectively; $a3 holds 1
bgt $a0, $a1, L1 # is al > bl?
bgt $a1, $a2, next # no: is BL > CL?
jbe next # no: skip next statement
L1: sw $a3, X # set X to 1
next:
We can use "fall-through" logic to keep the code as short as possible:
if (al > bl) OR (bl > cl)
X = 1;