## Slide 1: Integer Arithmetic: Multiply, Divide, and Bitwise Operations
Some material taken from Assembly Language for x86 Processors by Kip Irvine © Pearson Education, 2010
Slides revised 3/21/2014 by Patrick Kelley

## Slide 2: Overview
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction

## Slide 3
Shift and Rotate Instructions
Logical vs Arithmetic Shifts
sll and sllv Instruction
srl and srlv Instruction
sra and srav Instructions
rol Instruction
ror Instruction

## Slide 4
Irvine, Kip R. Assembly Language for x86 Processors 6/e, 2010.
Logical Shift
A logical shift fills the newly created bit position with zero:

## Slide 5
Arithmetic Shift
An arithmetic shift fills the newly created bit position with a copy of the number’s sign bit:

## Slide 6
sll and sllv Instruction
The sll (shift left) instruction performs a logical left shift on the destination operand, filling the lowest bit with 0.
Arithmetic left shift is identical to Logical, so no extra instruction is needed
# imm = bit positions to shift
sll Rd, Rt, imm
# low order 5 bits of Rs = positions to shift
sllv Rd, Rt, Rs

## Slide 7
srl and srlv Instruction
The srl (shift right) instruction performs a logical right shift on the destination operand. The highest bit position is filled with a zero.
# imm = bit positions to shift
srl Rd, Rt, imm
# low order 5 bits of Rs = positions to shift
srlv Rd, Rt, Rs

## Slide 8
sra and srav Instruction
The sra (arithmetic shift right) instruction performs an arithmetic right shift on the destination operand. The highest bit position is filled with the sign bit.
# imm = bit positions to shift
sra Rd, Rt, imm
# low order 5 bits of Rs = positions to shift
srav Rd, Rt, Rs

## Slide 9
rol Instruction
# low order 5 bits of Rs = positions to rotate
rol Rd, Rt, Rs
rol (rotate left) shifts each bit to the left
The highest bit is copied into the lowest bit
No bits are lost
Image shows an architecture where the highest bit is also copied into a carry flag.

## Slide 10
ror Instruction
# low order 5 bits of Rs = positions to rotate
ror Rd, Rt, Rs
ror (rotate left) shifts each bit to the right
The lowest bit is copied into the highest bit
No bits are lost
Image shows an architecture where the lowest bit is also copied into a carry flag.

## Slide 11
What's Next
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction

## Slide 12
Getting the carry bit
# works for shifts, rotates, or addu
addu $s4, $s1, $s2
stlu $s3, $s4, $s2 # $s3 now holds carry
Many useful shift/rotate apps rely on the carry bit
Since MIPS does not have status flags, we need a way
Assume unsigned, store result separately from source
If result < source, there was a carry.
sltu compares result and source, setting a register appropriately.

## Slide 13
Shifting Multiple Doublewords
Programs sometimes need to shift all bits within an array, as one might when moving a bitmapped graphic image from one screen location to another.
The following shifts an array of 3 words 1 bit to the right:
.data
array: .word 0x99999999h, 0x99999999h, 0x99999999h
.test
la $a0, array # load array address
lw $s0, ($a0) # load high word into $s0
srl $s1, $s0, 1 # shift
sltu $s2, $s1, $s0 # put carry in s2
sw $s1, $a0 # put shifted word back
# continued on next page

## Slide 14
Shifting Multiple Doublewords
# continued from previous page
addu $a0,$a0, 4 # add 4 bytes for next word
lw $s0, ($a0) # load middle word into $s0
srl $s1, $s0, 1 # shift
sltu $s3, $s1, $s0 # put carry in s3
ror $s2, $s2, $s2 # turn prev carry into mask
addu $s1, $s1, $s2 # add carry mask to word
sw $s1, $a0 # put shifted word back
# do last word
addu $a0,$a0, 4 # add 4 bytes for next word
lw $s0, ($a0) # load low word into $s0
srl $s1, $s0, 1 # shift
ror $s3, $s3, $s3 # turn prev carry into mask
addu $s1, $s1, $s3 # add carry mask to word
sw $s1, $a0 # put shifted word back

## Slide 15
Binary Multiplication
mutiply 123 * 36

## Slide 16
Binary Multiplication
We already know that sll performs unsigned multiplication efficiently when the multiplier is a power of 2.
You can factor any binary number into powers of 2.
  For example, to multiply $s0 * 36, factor 36 into 32 + 4 and use the distributive property of multiplication to carry out the operation:
$s0 * 36
= $s0 * (32 + 4)
= ($s0 * 32)+(EAX * 4)
li $s0,123
mov $s0, $s1
sll $s0, $s0, 5 ; mult by 25
sll $s1, $s1, 2 ; mult by 22
addu $s0,$s0, $s1

## Slide 17
Displaying Binary Bits
Algorithm: Shift MSB into the Carry bit; If CF = 1, append a "1" character to a string; otherwise, append a "0" character. Repeat in a loop for however big your data is.
.data
buffer: .space 33 # 32 byte string
.test
li $a0, 32 # doing a word
li $a2, ‘0’ # for output
li $a3, ‘1’
la $a1, buffer
# word was in $s0
L1: shl $s1, $s0, 1
sltu $s1, $s1, $s0
sb $a2, ($a1) # write ‘0’
beqz $s1, L2
sb $a3, ($a1) # overwrite ‘1’
L2: addiu $a1, $a1, 1 # next byte
addi $a0, $a0, -1 # next bit
bgtz $a0, L1 # loop until 0

## Slide 18
Isolating a Bit String
The MS-DOS file date field packs the year, month, and day into 16 bits:
li $a2, 0x0000000F # mask right 4 bits
lw $a0, date # load a date
srl $a0, $a0, 5 ; shift right 5 bits
and $a0, $a0, $a2 ; clear bits 4-31
sb $a0, month ; save in month variable
Isolate the Month field:

## Slide 19
What's Next
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction

## Slide 20
Multiply and divide
It should be apparent that multiplying two 32-bit numbers may produce a result larger than 32-bits
  In fact, it is possible to get a 64-bit result
  MIPS uses two special registers ‘high’ and ‘low’ to hold the entire result
Similarly, an integer division may result in both a quotient and a remainder
  Division by zero is undefined and you should check for this before you divide
  The quotient is stored in the ‘low’ register
  The remainder is stored in the ‘high’ register

## Slide 21
Multiply Instructions
No overflow is caught
Takes 32 cycles to execute (Booth’s algorithm)
There are macro versions with different arguments:
‘low’ register moved to a specified register
The latter two operations will also throw an overflow exception
mult Rs, Rt # remainder in high
multu Rs, Rt # quotient in low
mul Rd, Rs, Rt # result in high:low
mulo Rd, Rs, Rt # but low moved to
mulou Rd, Rs, Rt # register Rd

## Slide 22
Divide Instructions
No overflow is caught
Takes 38 cycles to execute
There are macro versions with different arguments:
‘low’ register moved to a specified register
No exceptions thrown; programmer must catch exception cases
div Rs, Rt # result in high:low
divu Rs, Rt # result in high:low
div Rd, Rs, Rt # result in high:low
divu Rd, Rs, Rt # but low moved to Rd

## Slide 23
What's Next
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction

## Slide 24
Extended Precision Addition
Adding two operands that are longer than the computer's word size (32 bits).
  Virtually no limit to the size of the operands
The arithmetic must be performed in steps
  The Carry value from each step is passed on to the next step.

## Slide 25
Extended Addition Example
Task: Add 1 to $s1:$s0
  Starting value of $s1:$s0: 0x00000000FFFFFFFF
  Add the lower 32 bits first, setting the Carry bit in $s2.
  Add the upper 32 bits.
li $s1,0 # set upper half
li $s0,0xFFFFFFFF # set lower half
addiu $s3, $s0, 1 # add lower half
sltu $s4, $s3, $s0 # check carry
move $s0, $s3 # put lower result in $s0
addu $s1, $s1, $s4 # add carry to upper half
# if both operands are bigger than a word, then
# you could add the upper halves and carry
# checking for a carry out each time.
    $s1:$s0 = 00000001 00000000

## Slide 26
Extended Subtraction Example
Task: Subtract 1 from $s1:$s0
  Starting value of $s1:$s0: 0x0000000100000000
  Subtract the lower 32 bits first, setting the Carry bit.
  Subtract the upper 32 bits.
li $s1, 1 # set upper half
li $s0, 0 # set lower half
Li $s5, 1 # number to subtract
subu $s3, $s0, $s5 # subtract lower half
sltu $s4, $s3, $s0 # check carry
move $s0, $s3 # put lower result in $s0
subu $s1, $s1, $s4 # subtract carry from upper half
$s1:$s0 = 00000000 FFFFFFFF